| REQUIREMENTS FOR URBAN BUSES (RUB) CHECKSHEET (Refer to RUB edition amendment no.3 December 2014) NB Not applicable for Section 8 Existing Bus Standards |
| --- |
| BUS [insert operator, bus make and model] | DATE [insert date] |
| Definition of bus | Measurement | Pass/Fail/ Score/ Comment |
| 2.2 Design and performance |
| Vehicle age < 20 years |  |  |
| 2.3 Engine |
| Acceleration 0-50km/h ≤ 30 seconds |  |  |
| Fuelling range = ≥ 350km or 15 hours |  |  |
| Emissions (current Vehicle Emissions Rule) |  |  |
| Noise (current Vehicle Equipment Rule) |  |  |
| Compartment insulation – Non-flammable material used. Fire to ISO 3795 or FMVSS 302 (US) or equivalent ECE standard |  |  |
| 2.4 Transmission |
| SB fully automatic or electronic shift |  |  |
| LB or LBDD fully automatic or electronic shift plus retarder |  |  |
| 2.5 Suspension |
| SB air suspension |  |  |
| LB/LBDD air suspension ECAS, including self-levelling |  |  |
| LB/LBDD kneeling at front ≥ 60mm drop/lift |  |  |
| Kneel or rise time <8 seconds |  |  |
| LB/LBDD driver controlled in-use indicator/drive off protection |  |  |
| 2.6 Stability and steering |
| LB/LBDD ESC-electronic stability control |  |  |
| 2.7 Braking |
| EBS and ABS |  |  |
| Vehicle movement above 5km/h is inhibited while rear door is open or the kneeling system is activated |  |  |
| 3.1 Access |
| Priority seats - 4 seats preferably off side Must be available when wheelchair space is occupied by wheelchair passenger or pram |  |  |
| Minimum of two forward facing |  |  |
| 3.2 Doors |  |  |
| SB one door >850mm single leaf |  |  |
| LB/LBDD two doors unless specifically for express/limited stop service |  |  |
| Front ≥ 1000mm |  |  |
| Rear ≥ 700mm, |  |  |
| LBDD Rear > 1000mm preferred |  |  |
| 3.3 Step height/depths |
| First step measured from the ground to top of step (not kneeled) |  |  |
| SB < 300mm, may be < 370mm if kneeling to < 300mm fitted |  |  |
| LB and LBDD Front < 370mm |  |  |
| Rear ≤ 370mm |  |  |
| Kneeled: Front 19.5 inch rims ≤ 280mm, 22.5 inch rims < 300mm |  |  |
| For LBDD internal step heights should be of equal height |  |  |
| Maximum of two different heights is permitted |  |  |
| 3.4 Floors |  |  |
| Slip-resistant(AS 3696.13) flooring used on floor areas |  |  |
| Front and rear door entry/exit step areas - contrasting colour |  |  |
| Multi-use/Wheelchair area - contrasting colour |  |  |
| Wheelchair wall mounted and flooring insert signage is required |  |  |
| Priority seat area - contrasting colour |  |  |
| SB flat floor at least to rear of priority area |  |  |
| LB/LBDD flat floor to rear edge of rear door or to front of the rear axle if only one door fitted on LB |  |  |
| LB/LBDD stepped access to saloon to the rear of the rear door maximum of 2 steps |  |  |
| LB/LBDD Is transverse ramp slope required to meet < 370mm rear step height |  |  |
| 3.5 Aisle width |
| SB > 780mm in middle of the wheel arch at height of 300mm |  |  |
| LB/LBDD ≥ 800mm through wheel arches and to rear of multi-use/wheelchair space |  |  |
| LB ≥ 440mm to rear of priority seats of saloon |  |  |
| LBDD > 440mm to rear of priority seats in both the lower and upper saloon |  |  |
| 3.6 Seating configuration |
| ≥ 60 percent forward facing |  |  |
| ≥ 50 percent forward facing in priority area |  |  |
| For LB rear ward facing seats fitted on front wheel arch |  |  |
| For LBDD rear ward facing seat fitted to the front and or the rear wheel arches |  |  |
| Seat spacing between forward-facing seats shall be ≥670mm |  |  |
| The height from the floor to the top of the front of the seat cushion should be ≥400mm and ≤500mm |  |  |
| The height to the top of the seat back excluding any grab handle should be ≥900mm |  |  |
| Are inwards facing flip up seats fitted if so location and number |  |  |
| Leg room > 300mm measured from front edge of seat squab horizontally to seat back or modesty panel in front |  |  |
| 3.7 Seating design |
| Seat width - single seat ≥ 425mm |  |  |
| Seat width - double bench or paired seat ≥ 875mm |  |  |
| Seat width - mother/child ≥ 760mm, location |  |  |
| Seat spacing - Forward facing ≥ 670mm |  |  |
| Seat style, frame or moulded shell |  |  |
| Seat styles, numbers of each - single (S), double (D) or triple (T) bench |  |  |
| Seat fabric, unpadded plastic, vinyl or fabric covered cushion or insert |  |  |
| 3.8 Luggage/stroller/prams/mobility devices |
| Provide space for 2 folded prams/mobility frames and 2 pieces of luggage of ≤25kg with dimensions ≤ 800mm x ≤ 300mm |  |  |
| 4.2 Vehicle interior, entrance and exit step and plinth edges |
| Door entry/exits - slip-resistant material |  |  |
| Sharks tooth design edging has not been used in any area |  |  |
| Step/edges and plinths fitted with yellow high-visibility, slip-resistant/non-trip nosing in a solid band contrasting colour |  |  |
| 4.3 Stanchions/handrails |
| High-visibility yellow contrasting colour |  |  |
| Along length of bus saloon(s) and not impede movement on aisle, spacing at least on alternate seats |  |  |
| Additional handrails in entry and exit locations |  |  |
| LBDD handrail/stanchions at top and bottom and in the stairwell area |  |  |
| Overhead contrasting colour handrails should be no higher than 1900mm from floor level, unless fitted with strap hangers to reach to or below this height |  |  |
| Maximum cross-section dimension 30-35mm |  |  |
| Finger/hand clearance space of 35-45mm between any part of the vehicle, and all part of a handrail |  |  |
| 4.4 Grab handles |
| Yellow contrasting colour if not an integral part of a moulded style seat back |  |  |
| Circular or cross section of 30-35mm |  |  |
| Length of 100mm-120mm |  |  |
| 4.5 Lighting |  |  |
| Internal entry and exit doorway ≥ 100 lux, externally downwards and outwards for >300mm |  |  |
| Entry/exit light automatically extinguished on door closure |  |  |
| Fare paying area ≥65 lux |  |  |
| LBDD Overhead lighting above the stairwell > 40 lux |  |  |
| LBDD stairwell sidewall low intensity safety lighting at each step height |  |  |
| General saloon behind driver's modesty panel ≥ 40 lux |  |  |
| 4.6 Security and safety |
| Wiring for CCTV - SB one located forward to the driver to view fare paying and saloon area |  |  |
| LB minimum of three, two internal and one external |  |  |
| LBDD minimum of 5 including two in upper saloon to view into the stairwell and saloon |  |  |
| Number of cameras provided - external, internal lower saloon, upper saloon |  |  |
| For LBDD signage requiring that “passengers must not stand in the stair well whilst the bus is in motion” |  |  |
| LBDD a nearside upper deck mounted tree guard |  |  |
| For LBDD an upper deck electro/optical approaching hazard warning device is optional |  |  |
| 4.7 Heating, ventilation and air conditioning |
| Adequate saloon heating and ventilation eg forced air system with a mix of hopper or sliding side windows and roof vents |  |  |
| For Auckland, Wellington and Christchurch, air conditioning climate control is mandatory |  |  |
| LBDD effective climate control in upper saloon is of great priority Passenger controlled individual directional vents are optional |  |  |
| 4.8 Demisting |
| If full air conditioning is not fitted, the demisting system must be capable of initial demisting and keeping clear glass panels of front and rear doors and all side windows |  |  |
| Communication |
| 5.2 Bus stopping signals |
| Fitted with 2 dual-indicator bus stopping signalling and display devices (a mix of upper and lower case) that are easily seen and heard by the driver and the passengers (one rear ward facing and a 2nd forward and rear ward facing repeater located near the rear door or rear axle if only one door fitted) LBDD Including one in the upper saloon |  |  |
| Easily reached by any person seated in a priority seating area or wheelchair area without having to stand up, eg on side walls or on stanchions |  |  |
| Used by elderly and disabled people with poor hand and finger function or dexterity |  |  |
| Adjacent to and not less than every second row of seats on both sides of the aisle |  |  |
| Fitted to the underside of any fold-up seat fitted in the multi-use/wheelchair space if the other bell push is obscured by the fold-up seat |  |  |
| The dashboard indicator shall have two components: a general signal and a second signal to indicate to the driver that the signal has been made by a passenger occupying a wheelchair or priority seating position |  |  |
| The device shall trigger both an audible and visual indication to the driver and passenger |  |  |
| Finger/thumb/knuckle push buttons on the vertical stanchions at a height of ≥1300mm and ≤1600mm above floor level |  |  |
| Finger/thumb/knuckle push buttons on the bus side panels at a height of ≥850mm and ≤1050mm particularly in the priority seating area or on the undersides of folding seats |  |  |
| Finger/thumb/knuckle push buttons fitted as near as possible to top edge of any fold up seat for use when seat in fold up position if the side wall button obscured |  |  |
| Note: Cordage alone is not acceptable |  |  |
| High contrast and consistent colours should be used ie. a red button on yellow background/mounting |  |  |
| 5.3 External destination display |
| A mix of upper and lower case is preferred for destination information |  |  |
| Front forward-facing three-digit/character route number and destination combination sign ≥1500mm wide located at or above the top of the windscreen |  |  |
| Near side, as close as possible to the front entrance, a route number and destination repeater sign preferably fitted at the top of the first side window |  |  |
| Rear ward-facing three digit/character route-number only sign at a height ≥1500mm and ≤2500mm ( for LBDD < 2900mm) above ground level and central or left of centre, ie toward the nearside of the bus |  |  |
| Front and rear route number characters shall be ≥150mm |  |  |
| Front destination characters shall be ≥125mm |  |  |
| Side destination characters shall be ≥60mm |  |  |
| For LB/LBDD a wide destination sign is desirable |  |  |
| 5.4 Internal information |
| Electronic information displays and announcements - ducting and mounting must be ready for fitment at a later date ( for LBDD includes upper saloon) |  |  |
| 5.5 Driver operational communication |
| For larger urban centres of larger fleets RT radio fitted |  |  |
| Facilities for passengers with impairments |
| 6.2 Priority seating area |
| Priority seating area well to the forward end of the saloon with at least four preferably all forward facing seats identified for passengers with impairments or extra mobility needs. These seats may be of the folding type in order to facilitate wheelchair access and stowage. Any fold-up seat must be capable of being held in the stowed position and be readily unlocked by simple and obvious mechanism. Non-lever systems are preferred |  |  |
| A separate space of dimensions not less than 800mm by 1300mm to cater for a wheelchair and user with a wheelchair footprint of ≤700mm width x ≤1200mm length |  |  |
| Contrasting, easily seen signage to indicate the area and request to vacate seats for use by passengers with disability/mobility needs along the following lines: ‘Priority seating area - Please vacate these seats for elderly or disabled passengers or parents/caregivers with small children’ |  |  |
| 6.3 Wheelchairs |
| Footprint to be provided for forward or rearward facing stowage ≤700mm width x ≤1200mm length |  |  |
| If transverse stowed, with handles and foot rest capable of being folded or stowed ≤700mm width x ≤900mm length |  |  |
| SB to carry a minimum of one rearward facing wheelchair, LB/LBDD a minimum of one rearward facing wheelchair (preferably on the nearside) |  |  |
| International wheelchair symbol for accessibility sign must be provided in the flooring material of any wheelchair space |  |  |
| 2 x wheelchair symbol signs externally fitted - one on left front of bus and one on side of bus by front door entrance |  |  |
| There should be signage to indicate wheelchair brakes and lap belts should be applied |  |  |
| Any passenger safety/modesty panel & vertical stanchion fitted behind wheelchair/multi-use space should not hinder wheelchair manoeuvrability in to/out of the space |  |  |
| 6.4 Boarding and alighting |
| Shall have a kneeling capability |  |  |
| The following shall be provided on the exterior of the bus adjacent to the front door: A sign stating ‘This bus kneels on request’ |  |  |
| 6.5 Ramp |
| A manually-operated flip-over style ramp >800mm width shall be provided at the front door |  |  |
| Ramp hinges & lifting rings/handles countersunk/flush with floor, preferably lifting handle full-hand width |  |  |
| Ramps must comply with section 8.2 of the Passenger Service Vehicles Rule 1999 in terms of any ramp, door brake interlock and driver warning system |  |  |
| High yellow contrast flat ramp edge marker strips are preferred over the raised metal edges |  |  |
| Ramp surface material must be slip-resistant |  |  |
| A wall mounted sign clearly indicating maximum permitted ramp weight and dimension for the wheel chair passenger, 300kg weight and 700mm width |  |  |
| Powered ramp fitted |  |  |
| 7. Driver compartment |
| A fully sprung driver's seat with adjustment for all three planes of driving position |  |  |
| A readily adjustable (tilt and height) steering wheel column and soft style easily cleaned, and dried steering wheel |  |  |
| A footrest for the left foot |  |  |
| Coat/jacket storage, eg hook |  |  |
| Out-of-sight storage for personal belongings such as bag/lunchbox |  |  |
| Ticketing equipment and till stand should be ergonomically located |  |  |

| Barrier protection panel immediately behind the driver to prevent any form of assault from behind, either directly by a passenger or by a thrown object |  |  |
| --- | --- | --- |
| A revenue collection and holding system so that the driver's cash can be readily and securely locked into a cash box that can be secured to the bus |  |  |

| Approval [insert bus make and model] |
| --- |
| Signature |  |
| Print name |  |
| Organisation |  |
| Position |  |
| Date |  |