## Slide 1: NZTA TTM Conference 2015 - Wairakei
High visibility garments

## Slide 2: CoPTTM Section B3 High visibility garments
High Visibility Garments:
Highlight changes in 4th Edition
Section CoPTTM Effective 1 January 2015
where TTMC label became TTMC–W
Introduce:
A New design
For a Traffic Controllers (TC) Garment

## Slide 3: CoPTTM Section B3 High visibility garments
A quick history
First High Visibility Garments made in NZ in the 90’s were
a New Zealand version of EN 471 design (for HCH).
In the late 90’s (‘97 & ‘99) the joint Aust & NZ Standards committee
published a Materials and a Garment Standard
- Early CoPTTM Designs based on these Standards
2010 and 2011 revisions were published for both these Standards.
2012 CoPTTM Section B3 updated to harmonise with the new Standards
A wider range of garment options were added to incorporate a number
of garments that had “appeared” in the market.
Garment design specifications established in conjunction with NZ’s
leading manufacturers

## Slide 4: CoPTTM Section B3 High visibility garments
CoPTTM Section B3
High visibility garments
High visibility materials and retroreflective fabrics must comply with
AS/NZS 1906 Part 4 2010
Part 4 High visibility materials for safety garments
both Fluoro and non fluoro
including the 2014 amendment
Garment designs are harmonised with but add to
AS/NZS 4602 Part 1 2011
Part 1 Garments for high risk applications
including the pending amendment
Compliance certificates

## Slide 5
CoPTTM Section B3 High visibility garments
High visibility garment design concept:
Each garment is appropriate for use:
in any weather condition, dry or rain
in daylight or the hours of darkness
and in low light conditions
The garment design specification:
CoPTTM Compliance set slightly higher than the minimum levels set in
Standards documents to recognise
the increased risk of accident
the frequent exposure to such risk and
the potential severity of the injury
Section B3 is a definitive design – not a minimum Standard

## Slide 6
CoPTTM Section B3 High visibility garments
Critical compliance points: (known by manufacturers)
Sewn in Label must state TTMC-W Compliant – incl Xtra Small
sizes
Test for compliance is the Size “S” Small garment – all in design
range must then be graded in proportion up and down
Area of background material is calculated as specified in
AS/NZS 4602.1 but to the area specified in CoPTTM.
Configuration of strips must comply with figures in Section B3
All garment designs must comply with both the specification
and Figures in Section 3
Compliance date = 1st January 2015. Current garments are good until no
longer appropriate for purpose.

## Slide 7
CoPTTM Section B3 High visibility garments
A point of note:
High Visibility Area Measurement
The International convention for high visibility measurement is the torso area only.
It does not include the sleeves area.
For high visibility garments the sleeves should morally maintain high visibility colour

## Slide 8
CoPTTM Section B3 High visibility garments
Last Garment on Vest style garment.
Area background fabric – 0.6m2 Area retroreflective fabric – 0.2m2
To: (for compliance size “S”)
Front - fabric area 0.21m2
Rear - fabric area 0.27m2
Retroreflective - per configuration
(panels and Tape)
Company logo area remains
Shirt tail remains at 150mm
Original CoPTTM Concept
Original CoPTTM Concept – Changes from:
Finished sleeveless vest garment forced to be too large for safety

## Slide 9
CoPTTM Section B3 High visibility garments
The Original Long Sleeved Garment
Now: (compliant “S” size)
Area remains at 0.6m2 = 0.3m2 front and back
Retroreflective configuration as indicated
Retroreflective additions permitted
Collar and sleeve colour
Becomes a Long Sleeved Coat

## Slide 10
CoPTTM Section B3 High visibility garments
Overalls option introduced
New: (for compliant size “S”)
Area = 0.6m2 = 3m2 front and back
Retroreflective configuration as indicated
Retroreflective additions permitted
Collar colour
and sleeve colour from below the elbow
Lower leg colour from a point above the knee

## Slide 11
CoPTTM Section B3 High visibility garments
NEW Miscellaneous Garment option
New: for compliant small size
Area as for Sleeveless vest
0.21 & 0.27m2
Retroreflective as indicated with shirt tail
Short Sleeve must be Orange
Long Sleeves colour change from below the elbow
Retroreflective alternative
Collar colour
Not tuck-in garment

## Slide 12
CoPTTM Section B3 High visibility garments
Traffic Controller TC Garment
The TC designation may not be worn all the time.
Its use:
In circumstances where an STMS is not on site or leaves to visit other sites*.
When the STMS is not present the Traffic Controller assumes control.
Therefore the Traffic Controller TC designation may be required at short notice and only until site control reverts to an STMS
*CoPTTM Section A Clause A5.9 Traffic Controller
NEW

## Slide 13
CoPTTM Section B3 High visibility garments
The TC Garment:
A standard orange high visibility garment (Class F or NF)
“TC” panel Front and back
Reversible Panel:
“TC” panel front
Garment orange on reverse
Traffic Controller Reversible Panel Concept
Designed to enable a Traffic Controller to always have it at hand – to be “available” at short notice.

## Slide 14
XYZ
ROADS
NZ
TC
CoPTTM Section B3 High visibility garments
Reversible TC Panel:
Front – Yellow Green retroreflective with black TC
Reverse – Garment Orange with Company Logo (Logo optional)
Clear pocket designed to hold TC Panel
Front left panel 100mm x 100mm
Centre back panel 100mm x 250mm
Traffic Controller – TC
Reversible panel concept
XYZ
ROADS
NZ
TC

## Slide 15: Thank You Questions
I am keen to have feed back regarding this concept