TRAFFIC MANAGEMENT PLAN

# RM 06 Intersection Marking – Letters and Symbols – 2 way flow

| Traffic Management Plan Reference |  |
| --- | --- |
|  | For Office Use Only |
| Organisation | Contractor Insert Contractor Name | Client Insert Client Name |
| Contract Name/Number | Insert Contract Name | RCA Consent Reference Insert Where Required |
| Location | Road Name(s) Insert Road Name | Road Level (LV, 1, 2, 3) Level 1 | Speed Limit Insert Speed Limit | From RP Insert R.P |
|  |  |  |  | To RP Insert R.P |
| Description of Activity | This is a static operation using two temporary lanes and a delineated work area for marking or remarking letters and symbols. |
| Work Programme | Insert Work Programme |
| Proposed/ Restricted Work Hours | Insert proposed or restricted hours of work |
| Traffic Details (Main Route) | AADT Insert AADT ex RCA | Peak Hour Flow Insert Peak Hour Flows ex RCA |

| Proposed Traffic Management Method | Active: Equipment: Advance Warning signs - Static TW1.4 “Road Marking” sign, with “Next Xkm’s” Supplementary Plate showing the length of closure(s) to a maximum of 4 km’s. Direction and Protection signs - RG17 “Keep Left” signs on temporary lanes. Works End signs - Static TW16 “Works End” signs on all site exits. TSL Signs - use if lane widths are narrowed below minimum for posted speed. Delineation 900mm cones are used for workplace delineation. 450mm cones may be used to protect wet markings. Method: TTM signs vehicles travel with the flow of traffic. Set out advance warning (and TSL if required) and works end signs. Establish two temporary lanes (one lane in each direction) using 900mm high cones with RG17 arrows to direct traffic. Lane width to be appropriate for posted speed or TSL. Mark protected letters or symbols. Removal of TTM equipment will follow the normal pattern of cones then signs. |
| --- | --- |
|  | Unattended: N/A |
|  | Night: As per “Active” above. |
| Proposed Speed Restrictions | Appropriate TSL for lane width. |
| Positive Traffic Management Measures | N/A |
| Contingency Plans | In the event of a “Major Incident” (Fatality, serious harm injury [real or potential] or significant property damage): The site will be secured to prevent the prospect of further injury or damage The emergency services will be notified The Engineer / RCA will be notified. In the event of an “Incident” (Non injury accident or structural failure of the road): The site will be secured to prevent the prospect of further injury or damage The Engineer / RCA will be notified. In the event of “Significant delays” to road users, (10 or more vehicles) the activity will be halted and equipment removed from the “live lane”. The activity will only recommence when the traffic queue has cleared and traffic volumes have reduced to a point where the delay is unlikely to be repeated. |
| Public Notification | N/A |
| Personal Safety | All staff will operate in terms of this approved Traffic Management Plan, the intent of the NZTA CoPTTM and the Company’s Health and Safety Management Plan for this type of operation. |
| On-Site Monitoring | All sites will be continuously monitored by the site STMS, site TC, site supervisor and / or other staff involved in the process and as dictated by the traffic volumes, weather conditions, etc. |
| Other Information (eg. delay calcs, EED issues, temporary speed issues, etc) | N/A |
| Layout Diagrams | See attached diagrams at back of this TMP. |
| EED Applicable? | No | Attached No |
| Traffic Controllers | Name (STMS): Insert details Cert No: Insert details | Phone (24 hours) Insert details |
|  | Name (TC) Insert details Cert No: Insert details | Phone (24 hours) Insert details |
| TMP prepared accurately to represent site conditions and submitted by | Contractor/Applicant Insert details Cert No: Insert details | Date Insert details |
| Requires Amendment | Engineer Insert details Cert No: Insert details | Date Insert details |
| This TMP is Approved on the Following Basis To the best of the approving Engineer’s judgment this TMP conforms to the requirements of the NZTA CoPTTM. This plan is approved on the basis that the activity, the location and the road environment have been correctly represented by the applicant. Any inaccuracy in the portrayal of this information is the responsibility of the applicant. The STMS for the activity is reminded that it is the STMS’s duty to “Postpone, cancel or modify operations due to the adverse traffic, weather or other conditions that affect the safety of this site” (reference A4.5). Approving Engineer: (Name and Certificate Number) (Signature) |
| Acceptance by TMC | TMC: Insert details Cert No: Insert details Signature: | Date: Insert details |

# Text boxes

Include a table with Temporary Lane widths